## Slide 1: METU INSTRUMENT
DC/DC CONVERTER
WITH FORWARD TOPOLOGY

## Slide 2: WHY DO WE SELECT FORWARD TOPOLOGY?
ADVANTAGES:
No air gap in transformer design
Less current ripple than flyback since filtered output
Lower current ripple due to larger magnetizing inductance

## Slide 3: WHY DO WE SELECT FORWARD TOPOLOGY?
DISADVANTAGES:
More components higher cost
In DCM gain changes too much
Higher voltage on mosfet and diodes

## Slide 4: TOPOLOGY SELECTİON
We decide to use Reset winding to increase efficiency
Select 100kHz,
Decrease ripple voltage
Increase response of controller

## Slide 5: Transformer Selection
R material has lower core loss than P material
E45959 is 2250 W core for 100kHz

## Slide 6: Transformer Design
Reset windings and Primary windings same, Max D=50%
Turn ratio is 2 satisfy output gain conditions.
Minimum turn ratio should be 3 to ensure no Saturation.

## Slide 7: Transformer Design
Select wire according to max current;
At min. input voltage,input current is 2A
Output current is 1A.
Since system not ideal, efficiency is not 100%,

## Slide 8: Transformer Design
Core Loss,
Copper Loss,

## Slide 9: Transformer Design
Window area=550 m^2.
K_fill=0.3 litz wire.
Calculations show max N is 70.
Most efficient N=8.

## Slide 10: Transformer Parameters

## Slide 11: MOSFET Consideration
Voltage drop is multiple of input voltage, since Reset Winding
- Vds>100V
Aimed efficiency is 85%, so max input current,

## Slide 12: Mosfet Consideration
IRF 740 N available component at lab.
R_on=0.55 ohm
t_on and t_off is much smaller than Ts

## Slide 13: HeatSink
TO-220 Package
ATS-PCB1020
Rc=6.4

## Slide 14: Component Selection
Output Inductor Consideration
This result is also verified by simulation, but in simulation higher value inductance are needed because of non-idealities.

## Slide 15: Output Inductor Selection
CG3885-ALB 470µH inductor is chosen according to simulation results.
It has 10 A max current and 8 mΩ max DC resistance.

## Slide 16: Output Capacitor Selection
This result is also verified by simulation, but in simulation higher value capacitor are needed because of non-idealities.

## Slide 17: Output Capacitor Selection
860080675012 150 µF capacitor is selected.
It has 0.05 Ω ESR value and 50 V DC voltage rating

## Slide 18: Diode Selection
Nearly 100 V has observed on diodes in simulation

## Slide 19: Diode Selection
For safety, 200 V 10 A diodes are chosen (DPG10I200PM)
It has 0.98 VF and 0.1 µC recovery charge
35 ns recovery time
-> Vf*If = 0.98V *3.2A = 3.13W conduction loss
QR*VR*fs = 2W switching loss

## Slide 20: Aimed Bonuses
Analog Controller IC: UC3844

## Slide 21: UC3844
Current Mode Controller
Voltage Feedback
Soft Start

## Slide 22: Efficiency Bonus
As simulated at Matlab efficiency is %85.

## Slide 23: Current Mode Control
Current control Mode control decrease
oscillations and output reach steady
state faster.

## Slide 24
Voltage Control Block

## Slide 25
Current Control Block

## Slide 26: PCB
We are planning to implement our nal circuitry on Printed Circuit Board (PCB). Because PCB has some advantages over stripboard. It is more professional than stripboard and it is less noisy. Also, after drawing proper PCB layout it is easy to implement.

## Slide 27: Soft Starting
Soft Starting Ciruit of UC3844

## Slide 28: Isolation
TLP250 Optocoupler